## Slide 1: BCUS101 – Bayesian Calibration Tutorial
A Integrated Workflow to Perform BCUS
Bayesian Calibration, Uncertainty Analysis and Sensitivity Analysis
on OpenStudio Models
July. 2016

## Slide 2: Read me
Limited number of output variables:
  Electricity:Facility
  Electricity:Building
  Gas:Facility
  Heating:Gas
  Heating:Electricity
  Cooling: Electricity
  Electricity:HVAC
Limited subset of uncertain parameters
Check the “Parameter UQ Repository V1.0.xlsx” for list of uncertain variables
Thermostat setpoint temperature cannot be calibrated due to the variation of setpoint within a daily schedule profile
Bayesian Calibration only calibrate one year of simulation with monthly utility data

## Slide 3: Overview
This tutorial will lead you through the procedures of applying BCUS - Bayesian Calibration, Uncertainty Analysis and Sensitivity Analysis on OpenStudio models.
Before you start, a functioning OpenStudio model and an EPW weather file are desired to illustrate the building and its surrounding environment being analyzed. Details of how to build an OpenStudio building model can be found here. Weather files can be downloaded here.

## Slide 4: Get Started
PREREQUISITE
INSTALLATIONS
Executing BCUS typically requires the following tools and packages:
OpenStudio
EnergyPlus
Microsoft Office(Some functions will be eliminated if using Libre Office in Ubuntu, i.e. drop down list)
R
R packages
SET ENVIRONMENT
Once the prerequisite tools are installed, set up the platform variables to access executables, examples and tests.
TEST INSTALLATION
To make sure BCUS runs correctly:
Test the Ruby-OpenStudio environment
Test installation by running a simple example
SIMPLE
EXAMPLES
Step by step following the tutorial which demonstrate the basic procedure of running BCUS.
Notes: - To use Ruby from OpenStudio Installation Package: Add path environmental variable: e.g., C:\Program Files\OpenStudio 1.6.0\ruby-install\ruby\bin
Install RubyXL: run cmd.exe as administrator, then gem install rubyXL

## Slide 5: Example File
Building Description
In the Example folder, users can find the ExampleBuilding.osm model with required input files in order to run BCUS.
The example building is a 3-story, 100,000 sqft office building located in PA. It has a rectangular footprint and 50% window-to-wall ratio. The heating, ventilation and air conditioning system in the building is VAV system with DX cooling (COP =2.6). The electric resistance serves the central heating and reheat in the VAV system.

## Slide 6: Examples
Create a Project Folder
The BCUS Package is distributed in the format of a zip folder named “BCUS.zip", the first step is to extract the folder to a local directory on your computer. The main folder contains 4 subfolders as shown below.
BCUSCode: Ruby codes to run the program
Install: Help first time users install the required packages, setup
the path and check the status of the installation
Example: The example building model and required inputs
Tutorials: Tutorial document

## Slide 7: Examples: Input Files Format
Input Files
Create a project folder inside the main folder
Copy the files in: …\BCUS\Example and paste them to the project folder. Now you would see the the following files in your project folder.
After pasting the seven required input files for Bayesian calibration, replace the ExampleBuilding.osm with your building model; replace the .epw file with the weather file for your building’s location, replace the Prior.csv and Utility.csv with your building’s information if applicable.

## Slide 8: Step 1: Create Prior Uncertainty File
Parameter Type | Object in the model | Parameter Base Value | Distribution | Mean or Mode | Std Dev | Min | Max
Infiltration | FlowPerExteriorArea |  | Triangle Absolute | 0.00095 |  | 0.000319444 | 0.002894444
Lights_WattsPerSpaceFloorArea | Office_Space_Type | 15.17433543 | Normal Absolute | 15.17433543 | 5 | 0 | 35
PlugLoad_WattsPerSpaceFloorArea | Office_Space_Type | 8.072932813 | Normal Absolute | 8.072932813 | 5.14001398 | 0 | 20.56
People_SpaceFloorAreaPerPerson | Office_Space_Type | 18.58060872 | Normal Absolute | 18.58060872 | 3 | 0 | 10
Open …Example/SA_Output/UQ_Building_name.csv
Change the distribution to Triangle/Normal Absolute.
Assign prior distribution parameters for each selected sensitivity parameter.
Make sure the required prior distribution information is correct
Save the file as Prior.csv in your project folder (do not change the name), here we save it to: …/BCUS/Example
Change the distribution accordingly
Assign prior distribution parameters

## Slide 9: Step 1: Create Prior Uncertainty File (Cont.)
Parameter Type | Object in the model | Parameter Base Value | Distribution | Mean or Mode | Std Dev | Min | Max
Infiltration | FlowPerExteriorArea |  | Triangle Absolute | 0.00095 |  | 0.000319444 | 0.002894444
Lights_WattsPerSpaceFloorArea | Office_Space_Type | 15.17433543 | Normal Absolute | 15.17433543 | 5 | 0 | 35
PlugLoad_WattsPerSpaceFloorArea | Office_Space_Type | 8.072932813 | Normal Absolute | 8.072932813 | 5.14001398 | 0 | 20.56
People_SpaceFloorAreaPerPerson | Office_Space_Type | 18.58060872 | Normal Absolute | 18.58060872 | 3 | 0 | 10
In case that the sensitivity analysis is not a prerequisite, the user need to make sure the input format in Prior.csv obey the form in the image below.
Assign prior distribution parameters for each selected sensitivity parameter.
Make sure the required prior distribution information is correct
Save the file as Prior.csv in your project folder (do not change the name), here we save it to: …/BCUS/Example
Change the distribution accordingly
Assign prior distribution parameters

## Slide 10: Step 2 Calibration Parameters Selection (Not a mandatory step)
SA on Total Gas Use
SA on Total Electricity Use
We first run a sensitivity analysis to select top ranking parameters which have significant impact to the simulation output. In this example, we will take the results directly from previous sensitivity analysis.
Navigate to …/Example/SA_Output folder and open:
SA_wrt_Electricity.Total.End.Uses..GJ..csv
SA_wrt_Natural.Gas.Total.End.Uses..GJ.csv
Select parameters with high rankings according to mu.star.
In this example, we select the infiltration rate, plug load and occupancy load respectively.
Notes: If you not sure which parameter you want to calibrate, skip to slides blahblah

## Slide 11: Step 3: Create Utility/Measurement file (Monthly)
Create the Utility.csv file in your project folder and save the monthly measurement of electricity and gas in the .csv file.
Note: The unit of the measurement data is required to be converted to [J].

## Slide 12: Step 3: Edit Executable Bash/Batch Script
Open Bayesian_Calibration.bat file using any available text editing software:
Replace current directory with your “BCUS” directory, such that:
export BCUS =“<your main folder directory>”
Replace current file names with your building model name and weather file name.
You can save the modified bash script with a new name, such as Run_Calibration.bat or just keep the old name.
Replace with the directory of your main folder
Replace with the name of your
building model
Replace with the weather file of your building model

## Slide 13: About the Bash Script
--osmName: The name of the OpenStudio model (.osm)
--epwName: The name of the weather file(.epw)
--outfile: The name of the simulation output setting file (.csv)
--priors: Prior uncertainty distribution table (.csv)
--utilityData: Utility data (.csv)
--numLHS: The number of sample points of Monte Carlo simulation with Latin Hypercube Design
--seed: Need to be an integer. If same, the sequence of the samples will be the same
--noCleanup: If true, intermediate files will be kept
--verbose: If true, run in verbose mode with more output info printed
--comFile: Filename of computer simulation outputs (.txt)
--fieldFile:Filename of utility data measured from the field meter for comparison (.txt)
--numMCMCSteps: The number of MCMC steps. The number should be large enough to derive a
good approximation of posterior distribution.
-- numOutputVars: The number of output variables used for calibration. 1 for either electricity or
natural gas; 2 for both electricity and natural gas
--numWVars: The number of weather variables
--numBurnin: The number of burning samples to dump in initial steps of MCMC. Suggested value: 10%
NumMCMC
--postsFile: The filename of posterior distributions (.csv)
--pvalsFile: The filename of pvals (.csv)
--help: Display help

## Slide 14: Step 3: Run Executable Bash Script in the Terminal
Launch the Terminal in your operating system:
For OSX – Press Command + Space and type terminal and press Enter
For Linux – Open the Dash by clicking the Ubuntu icon in the upper-left, type terminal, and
select the Terminal application from the results that appear.
or simply hit the keyboard shortcut Ctrl-Alt+T.
For Windows – Click Start, in the search box type cmd and press Enter
Navigate to your project folder
Click the cursor in your Terminal/cmd type:
cd <your project folder directory>
For example,
  cd /Users/username/Documents/OpenStudio/BCUS/Example
Run the bash script you just modified by type:
Bayesian_Calibration.bat (Windows)
sh Run_BC.sh (Linux/OSX)

## Slide 15: Output Files
Output Files
The Output files for Bayesian Calibration are generated in the .../Calibration_Output folder.
Plots of prior and posterior distributions of calibration parameters
Example plots of posterior

## Slide 16: Interpretation of the results
The peak of the distribution shifts to the left
The full range
The most likely region also reduce

## Slide 17: Interpretation of the results
Uncertainty didn’t reduce much, The peak didn’t shift
The mean shifted the sd didn’t change much, the most probably shift to the right